## Slide 1: Java with Raspberry Pi
Stephen Chin (@steveonjava)
Java Technology Evangelist
JavaOne Conference Chair
James Weaver (@javafxpert)
Java Technology Evangelist

## Slide 2: Java Scale
Raspberry Pi Coffee

## Slide 4: Java Scale

## Slide 7
Driving Test
https://www.flickr.com/photos/davidyuweb/1352312273

## Slide 14: Up-Up-Down-Down-Left-Right-Left-Right B, A, Start

## Slide 15: Meet Mr. Grabby
https://www.flickr.com/photos/pasukaru76/8278458818/
https://www.flickr.com/photos/fallentomato/5656700432/
+
=

## Slide 16: Meet Mr. Grabby

## Slide 17: Mr. Grabby's Back
Controller
Grabber

## Slide 18: Controller
Raspberry Pi
Cooking Hacks Shield
MakeBlocks ME Base Shield

## Slide 19: Mr. Grabby's Belly
Line Follower
Batteries
DC Motors

## Slide 20: How Line Followers Work
Infrared LED
  Bounced light off the ground
Infrared Luminosity Sensor
  Detects reflected light

## Slide 21: Getting GPIO
gpio = GpioFactory.getInstance();
lineFollowA = gpio.provisionDigitalInputPin( RaspiPin.GPIO_13, "LineFollowA");
lineFollowB = gpio.provisionDigitalInputPin( RaspiPin.GPIO_14, "LineFollowA");
startGPIO(); boolean leftSensor = lineFollowA.getState().isHigh();
boolean rightSensor = lineFollowB.getState().isHigh();

## Slide 22: Line Following Algorithm
if (leftSensor && rightSensor) { //we are lost
doDrive(lineLocation);
} else if (!leftSensor && !rightSensor) { //on the line
lineLocation = Drive.forward; doDrive(Drive.forward);
} else if (!leftSensor && rightSensor) { //off the right
lineLocation = Drive.left; doDrive(Drive.forward);
} else if (leftSensor && !rightSensor) { //off the left
lineLocation = Drive.right; doDrive(Drive.forward);
}

## Slide 23: Make your own Mr. Grabby
MakeBlock Advanced Robotics Kit
MakeBlock ME Base Shield
Cooking Hacks Shield
USB Battery (1A)
Code here:
https://github.com/steveonjava/LineFollower

## Slide 24
IoT Magic

## Slide 25: Wearable Raspberry Pi
ODROID-W
  Raspberry Pi clone
NFC/RFID Sensor
  Adafruit PN532 chipset
RFID Playing Cards
  Mifare Ultralight tags embedded
IoT Magic Hat

## Slide 27: RFID/NFC Reader Configuration
Pi configuration
  I2C, SPI, or UART
NFC configuration
  libnfc to interface with the NFC reader.
  pcscd to expose rfid readers to Java SE
  idfnfc to bridge libnfc to idfnfc
Java hacking
  smartio API that is already a part of the JRE.

## Slide 28: Getting a Card Terminal
TerminalFactory factory = TerminalFactory.getDefault();
CardTerminals terminals = factory.terminals();
List<CardTerminal> list = terminals.list();
CardTerminal cardTerminal = list.get(0);

## Slide 29: Waiting for a Card
while (true) {
cardTerminal.waitForCardPresent(0);
handleCard(cardTerminal);
cardTerminal.waitForCardAbsent(0);
}

## Slide 30: Read Data
card = cardTerminal.connect("*");
CardChannel channel = card.getBasicChannel();
CommandAPDU command = new CommandAPDU(getAddress);
ResponseAPDU response = channel.transmit(command);
byte[] uidBytes = response.getData();

## Slide 31: Ultimaker 2

## Slide 33: Java Constructive Geometry (JCSG / JFXScad)
Create geometries from pure Java code
Visualize with a JavaFX user interface
Generate STL files for 3D printing
Project sites:
https://github.com/miho/JCSG
https://github.com/miho/JFXScad

## Slide 35: New Book Announcement
Raspberry Pi with Java

## Slide 36
Stephen Chin
tweet: @steveonjava
blog: http://steveonjava.com
nighthacking.com
Real Geeks
Live Hacking
NightHacking Tour